Potential divider circuits

# Text boxes

# V2

V = V1 + V2

IR = IR1 + IR2     V2 = IR2

and so

V2 = R2/[R1 + R2]

Digital voltmeter

Very high resistance

Analogue voltmeter

Much lower resistance

R1

R2

I

I

V2

V1

### V

### V

V2

V1

R2

R1

# V2

Virtually no current flows through the voltmeter

More current flows through the voltmeter